## Slide 1: TVAA KA Re-flash Method
For R-Theme Coaching application development environment
2018/02/02

## Slide 2: TVAA DA Re-flash Method
Software re-flash for TVAA DA needs the below 5 step sequence.
USB drive Setup
Software Update
Parameter Update
Data Reset (All Data Clear)
Version Check
During STEP2 through STEP3, some error message will be displayed such as “Unfortunately HOME app has stopped”.
However these errors are caused by mismatch between software and parameter.
Please ignore these error messages during the re-flash process.
※Caution
→After the data reset, Anti-theft screen will be displayed.
VIN information is required to unlock Anti-theft.
Please turn ENG or IG on to unlock Anti-theft.
No need.

## Slide 3: ■STEP1：USB drive Setup
USBメモリをPCに挿してください.
CL - MH17N2AX フォルダの中の“SoftwareUpdate_20180202”をUSBメモリにコピーしてください.
コピーが終わったらUSMメモリを抜いてください.
■用意するもの
4GBかそれ以上のUSBメモリ
Windows7以上のPC
アップデート用のファイル(folder name is “SoftwareUpdate_20180202”)
USB directory tree
USB drive root
└── CL-MH17N2AX
└── force_loading.zip

## Slide 4: ■STEP2：Software Update
(1) D/AのUSBポートにUSBメモリを挿してください
(2) ホーム画面を開いてDealer Diagnosisの中のVersion screenを開いてください.
Home Screen
Diagnosis Menu
Detail Information & Setting
Version Screen
5秒間押し続けてください
[HOME]+[POWER]+[SOURCE]
“Detail Information & Setting”
をタップ
“Version”
をタップ
HW Key Operation
Touch screen Operation
No need to operate
(値はサンプルです.)

## Slide 5: ■STEP2：Software Update
(3) アップデートを開始してください(約10分かかります.)
アップデートが走っている最中は絶対に電源を落とさないでください.
Version Screen
“Loading”
をタップ
“Install”
をタップ
Loading Screen
VUP Confirmation screen
Before start installing,
please check the SW version with expected or not.
SoC(Android) : 1800-1849-000_local_20180131.1204
Amigo : --------
System μCOM : B365
※Warning
“OK”
をタップ
しばし待たれよ
Downloading
Updating
(値はサンプルです.)
(These values are example)

## Slide 6: ■STEP2：Software Update
(4) アップデート完了後、自動で再起動します.
再起動
Updating
Start up logo
After starting up, some error message will be displayed such as “Unfortunately HOME app has stopped”.
However these errors are caused by mismatch between software and parameter.
Please ignore these error messages during the re-flash process.
※Caution
“OK”
をタップ
-> 次のページへ
Disclaimer
Home Screen

## Slide 7: ■STEP4：Data Reset(All Data Clear)
(1) 再起動後, Dealer Diagnosisの中のBackup Data Clear画面を表示してください.
Home Screen
Diagnosis Menu
5秒間押し続けてください
[HOME]+[POWER]+[SOURCE]
“Detail Information & Setting”
をタップ
“Functional Setup”
をタップ
“Backup Data Clear”
をタップ
Detail Information & Setting
Functional Setup
Backup Data Clear

## Slide 8: ■STEP4：Data Reset(All Data Clear)
(2) “All Data Clear”を実行してください
Backup Data Clear
All Data Clear Confirmation popup
“All Clear”
をタップ
“Yes”
をタップ
“Yes”
をタップ
Sometimes, it takes more than 10 sec till start reset
after pressing “Yes”.
Even that happen, please wait for a while without any operations.
Reset
All Data Clear Re-Confirmation popup
Data Resetの間は絶対に電源を落とさないでください.
※Warning

## Slide 9: ■STEP5：Version Check
再起動後、 Dealer Diagnosisの中のVersion screenを開いてください.
Home Screen
Diagnosis Menu
Detail Information & Setting
Version Screen
5秒間押し続けてください.
[HOME]+[POWER]+[SOURCE]
“Detail Information & Setting”
をタップ
“Version”
をタップ
Please check the final version is correct with expected.
(See next page.)

## Slide 10: ■STEP5：Version Check
Version Screen
①
②
③
① |  | Build Number | SoC Software version | sakura.1800-1849-000_local_20180131.1204
② |  | product ID | Vehicle Parameter type & version | 17N2AX10
③ | ③-1 | SYS Soft Version | SYS Software version | B365
 | ③-2 | SYS SetID Version |  | 0500
 | ③-3 | SYS Data Version | SYS Parameter type & version | 0216

## Slide 11: ■FAQ
# | Q | A
1 | “There are no update programs. Please try again.” message is displayed. And doesn’t start version up on STEP2 with the below screen after pressing “Loading” button. | Version up file name or folder name in STEP2 USB is not match with DA. →Need to use other version up data. Please tell to Panasonic with “Product ID” in Version Screen and folder/file name in USB.
2 | “There are no update programs. Please try again.” message is displayed. And doesn’t start version up on STEP2 or STEP3 with the below screen after pressing “Install” button. | Version up file in STEP2 or STEP3 USB is not match with DA. →Need to use other version up data. Please tell to Panasonic with “Product ID”